## Slide 1
Tesseract Journal Extension
Revision Briefing
ACM Transactions on Spatial Algorithms and Systems
Manuscript: Tesseract, Generating Indoor Graph Maps from Large-Scale Low-Semantic Floor Plans
Overview of the reviews, the work completed in response, and the state of the revision.
Revision due September 6, 2026

## Slide 2
Summary of the Reviews
Tesseract Journal Extension, Revision 1
2
All three reviewers recommended major revision, and all three considered the work publishable after improvement. None questioned the technical soundness of the pipeline. The concerns focus on the distance between what the paper claims and what it currently demonstrates.
• Reviewer 1 found the paper well written and relevant. The two most substantive concerns were that Algorithm 1 does not guarantee the property the text states, and that the multi-floor extension, as realized, is too simple to carry the journal delta.
• Reviewer 2 was broadly positive about the decomposition and the room-family mechanism, and listed seven specific weaknesses, mainly around automation clarity, the corridor-door failure mode, missing ablations, and the fidelity metric.
• Reviewer 3 saw a valuable practical contribution and asked for repositioned contributions, restored dataset breadth, a baseline comparison, tempered automation claims, and concrete action on the dominant failure mode.

## Slide 3
Common Themes Across the Three Reviews
Tesseract Journal Extension, Revision 1
3
Four themes appear in more than one review, and they shaped the priorities of the revision.
1. Automation. The multi-floor correspondence was hand-written and then validated, which the reviewers felt did not match the automation language in the paper.
2. The corridor-door failure mode. The paper diagnosed missed corridor doors as the dominant failure but offered only a projection rather than a measured treatment.
3. Evaluation breadth and rigor. The journal version evaluated fewer sites than the conference paper, lacked ablations, and had no baseline comparison.
4. Measurement quality. The Euclidean fidelity proxy and the nominal inter-floor weights were both questioned as references for route quality.

## Slide 4
Approach Taken in the Revision
Tesseract Journal Extension, Revision 1
4
We treated the reviews as a specification for the system as much as for the text. Where a claim was ahead of the implementation, we extended the implementation. Where a result was asserted, we measured it. Where a metric was questioned, we replaced it with a more objective one.
• The manual inter-floor mapping is replaced by an automatic matching module, and the existing validation rules now verify the machine's output.
• The funneling guarantee is corrected, formally stated, and proven, with the difference from the earlier claim measured and reported.
• Eleven new or extended experiments support the contested claims, covering degradation, ablations, fidelity, density, text accuracy, downstream tasks, and a baseline.
• Every change in the manuscript is color-coded by the reviewer who motivated it, and every response in the letter is localized by section, subsection, and figure or table number.

## Slide 5
Reviewer Requests on the Paper, Part 1
Reviewer requests, grouped
5
Positioning and claims
• Position the extension around multi-floor graph construction and the room-family representation, and do not present door classification as a new contribution (R3.1a, R3.1b).
• Temper the automation claims, since a hand-written mapping plus filename metadata is not automatic inference (R1.9, R2.W1, R3.2).
• Narrow the general applicability language to the actual input assumptions (R3.4).
Definitions and mechanisms
• State the underlying representation explicitly (R1.2).
• Define exit doors and clarify directionality (R2.W4).
• Clarify corridor identification and the handling of unlabeled corridors (R2.W5).
• Describe the actual OCR error-handling mechanism (R1.11).

## Slide 6
Reviewer Requests on the Paper, Part 2
Reviewer requests, grouped
6
Presentation and rigor
• Include a figure showing the floor plans used in the evaluation (R1.5).
• Introduce every acronym at first use (R1.10).
• Define or remove the term semantic centroid (R1.17).
• Repair the node-placement figure whose panels are inconsistent (R1.13).
• Replace the box plot that cannot show a bimodal distribution (R1.16).
• Move a results paragraph out of the methods section (R1.15).
• Justify the use of label positions as main-node positions (R1.3).

## Slide 7
Reviewer Requests on the Experiments, Part 1
Reviewer requests, grouped
7
Correctness and guarantees
• Algorithm 1 does not guarantee main-node routing, so state and prove the property that actually holds (R1.4).
• Add ablations that isolate funneling, transition preservation, pruning, and the multi-floor validation constraints (R2.W6).
The dominant failure mode
• Go beyond the recovery projection for missed corridor doors, through a stronger model, a recovery ablation, or a topological repair strategy (R2.W3, R3.3).

## Slide 8
Reviewer Requests on the Experiments, Part 2
Reviewer requests, grouped
8
Measurement quality
• Replace the Euclidean fidelity proxy with a navigationally realistic reference (R1.7, R2.W7, R3.5).
• Address the nominal inter-floor transition weights that can distort cross-floor fidelity (R3.5).
Breadth and baselines
• Evaluate more than one building and restore the conference sites (R1.6, R2.W2, R3.1c).
• Compare against at least one competing approach (R3.1c).
Unreported numbers
• Report text label detection and recognition accuracy with failure consequences (R1.8).
• Justify corridor node density with measurements (R1.1).

## Slide 9
Stage 1. Automatic Inter-Floor Transition Matching, Method
Addresses R1.9, R2.W1, R3.2 - Section 9.2
9
This stage addresses the shared concern that the multi-floor correspondence was manual. The system now infers which stairs and elevators on adjacent floors are the same physical shaft, in two steps.
• Registration. The two floor drawings are aligned by a similarity transform. Candidates come from four generators, including phase correlation of glyph-filtered wall masks and a drawing-scale prior derived from detected door widths. Candidates are ranked by a symmetric coverage-gated chamfer distance on wall evidence and refined by least squares and iterative closest point.
• Assignment with rejection. A global optimal assignment pairs shafts across floors, and an explicit rejection option leaves a shaft unmatched when no pairing is good enough, which is the appropriate outcome for a stairwell that terminates.
The hand-written mapping file remains available as an override, and the validation rules now verify the inferred result.

## Slide 10
Stage 1. Automatic Inter-Floor Transition Matching, Results
Addresses R1.9, R2.W1, R3.2 - Section 10.8, Figures 7 and 8
10
• Under controlled perturbations of a real floor, matching accuracy is 1.000 on every sweep, through 400 pixels of translation, 30 degrees of rotation, scale factors from 0.7 to 1.4, twin shafts down to 25 pixels apart, and shaft-deletion tests.
• A greedy nearest-neighbor baseline drops to 0.75 accuracy on close twins, which shows the benefit of solving the assignment globally.
• Median registration recovery error is 0.5 pixels under translation, 4.4 under rotation, and 4.9 under scale.
• On a genuinely different floor pair, the system accepts one supported correspondence at confidence 0.83, leaves every other shaft unmatched, and records explicit warnings in the mapping provenance. This conservative behavior is the intended outcome for partially overlapping sections.

## Slide 11
Stage 2. Room-Family Funneling, Correction and Proof
Addresses R1.4 - Section 7.3
11
Reviewer 1 observed that Algorithm 1 does not guarantee that subnode-to-door paths pass through the main node. The observation is correct, and we confirmed it in our own implementation, where 69 of 186 such shortest paths bypass the main node on the primary evaluation floor.
• The claim is replaced by the property that actually holds and that routing actually needs, namely complete intra-room connectivity at a linear number of intra-room edges.
• Algorithm 1 is rewritten to describe the construction as implemented, a transient proximity lattice with an anchor-rooted shortest-path tree and one shortcut edge per door.
• A new Proposition with proof establishes the guarantee, and the bypass behavior is described openly as intentional, since the shortcut edge shortens realized paths.

## Slide 12
Stage 2. Room-Family Funneling, Ablation Results
Addresses R1.4, R2.W6 - Section 10.4, Table 3
12
A three-way ablation compares the construction against a dense wiring upper bound and a single-node-per-room lower bound on the same floor.
Variant | Intra-room edges | Completeness | Route stretch
Dense wiring | 1,869 | 1.000 | 1.000 reference
Funneling, ours | 167 | 1.000 | 1.072
One node per room | none | 1.000 | 1.135, no spatial detail
• A second floor yields exactly one intra-room edge per subnode, which matches the bound in the Proposition.
• The complexity analysis is now explicit, with 963 shortest-path computations completing in 2.0 seconds on the primary floor.

## Slide 13
Stage 3. Door-Detector Degradation Study, Method
Addresses R2.W3, R3.3 option (b) - Section 10.3
13
The reviewers asked for a measured treatment of the dominant failure mode, missed corridor doors, in place of the earlier projection.
• The study deletes doors from the pre-pruning graph, where the full corridor and room mesh is intact, and measures pairwise room completeness and exit reachability.
• Deletion runs from zero to fifty percent of detected doors, with twenty Monte-Carlo draws per level, both at random and restricted by door type.
• A per-door sensitivity analysis additionally deletes each corridor-to-corridor door on its own, which attributes the damage to individual doors rather than to a percentage.

## Slide 14
Stage 3. Door-Detector Degradation Study, Findings
Addresses R2.W3, R3.3 - Section 10.3, Figure 3, and Section 11
14
The findings refine the original claim in a useful way.
• Room-to-corridor deletions reduce completeness steadily, because each room depends on a single access door.
• Most corridor-to-corridor doors prove redundant, since the corridor mesh reconnects around them.
• The damage concentrates in bridge doors. On one evaluation floor, a single such door accounts for 0.51 of pairwise completeness and 0.54 of exit reachability on its own.
• Bridge doors coincide with the cut vertices of the graph, so the vulnerable doors can be identified mechanically. This turns the failure mode into a targeted verification problem, and the discussion outlines image-guided repair as future work.

## Slide 15
Stage 4. Route Fidelity, New Reference
Addresses R1.7, R2.W7, R3.5 - Section 10.6
15
The reviewers questioned the Euclidean distance proxy, and we agreed with the analysis. The revision validates route quality against free-space geodesics, the exact shortest walkable paths through the drawing's non-wall pixels, with doorways opened at detected door positions.
• Two variants bracket the truth, a permissive bound over all free space and a conservative bound that excludes the semantic outside class.
• Rendered overlays draw each geodesic and graph route on the floorplan, so the reference paths can be verified visually.
• The measured ratio of geodesic to Euclidean distance runs from 1.35 to 1.67 on average and reaches 3.3, which quantifies why the earlier proxy was a weak reference.

## Slide 16
Stage 4. Route Fidelity, Results
Addresses R1.7, R2.W7, R3.5 - Section 10.6, Figure 6
16
• On the primary enclosed floor, graph routes are within 4.7 percent of the optimal walkable paths on average, with a ninetieth percentile of 9.3 percent, and the two reference bounds agree.
• On the more open section, the conservative bound gives a mean stretch of 1.24 and the permissive bound gives 2.30. The gap between the bounds quantifies sparse outdoor routing, which the discussion now states as a limitation.
• The verification overlays are included with the revision, and a sample appears in the manuscript as Figure 6.

## Slide 17
Stage 5. Physical Inter-Floor Edge Weights
Addresses R3.5 - Section 9.3 and Section 10.8
17
Reviewer 3 noted that nominal transition weights can distort cross-floor fidelity, and the observation was correct. Inter-floor edges now carry modeled vertical travel instead of a unit cost.
• The weight is the product of a travel factor, a 4-meter story height, and the drawing scale in pixels per meter. The scale is estimated from detected door widths under the standardized 0.9-meter leaf, with factors of 2.2 for stairs and 1.0 for elevators.
• The scale estimates are independently consistent across floors, at 31.1 versus 32.2 pixels per meter, which supports the estimation approach.
• The correction changes the measured step-free detour ratio from 2.02 to 1.79, so the earlier unit weights had visibly inflated cross-floor costs.
• The same scale estimate also serves as a registration prior in the matching module.

## Slide 18
Stage 6. Corridor Sampling Density
Addresses R1.1 - Section 10.5, Figure 5
18
Reviewer 1 asked why corridors need dense node coverage. We reran the full pipeline at grid spacings from 20 to 80 pixels and measured the trade-off directly.
Spacing | Nodes | Completeness | Route error versus 20 px
20 px, default | 878 | 1.000 | reference
60 px | 375 | 1.000 | 4.6 percent
80 px | 339 | 0.492 | 163 percent
The reviewer's intuition is confirmed, since moderate density preserves both connectivity and route quality. The failure at 80 pixels is abrupt rather than gradual, so the denser default provides a safety margin against narrow corridors at a known and now-stated cost.

## Slide 19
Stage 7. Pruning Ablations
Addresses R2.W6, R1.14, R1.15 - Section 10.4, Figure 4
19
Reviewer 2 asked for component-level ablations of the pruning stage, and Reviewer 1 asked whether the transition protection is ever needed. Both questions are answered by re-deriving the keep-set with individual terms disabled.
• Removing the transition keep-term removes every transition from the pruned graph, and removing the exit term removes every exit door, so each term is individually necessary.
• The full pruning pass removes 59 percent of nodes and 82 percent of edges, from 2,139 to 878 nodes and from 6,262 to 1,118 edges.
• Measured route inflation is exactly zero, because kept paths are shortest paths by construction, and the mean query time improves from 2.10 to 0.50 milliseconds.
• The paragraph that previously justified this design inside the methods now closes the pruning analysis in the evaluation, as Reviewer 1 requested.

## Slide 20
Stage 8. Text Accuracy and Vocabulary Matching
Addresses R1.8, R1.11, R2.W5 - Sections 5.2 and 10.2
20
Reviewer 1 asked how well label extraction works and what happens when labels are missed. We measured both against a hand-enumerated ground truth of every visible label.
• Detection finds 43 of 43 labels, and recognition is exact for 41 of 43, which is 95.3 percent. Both failures truncate a leading digit of a room number, so the room node survives with an incorrect name and connectivity is unaffected.
• A label missed entirely leaves its region without a semantic seed. An unlabeled variant of the same drawing demonstrates this case by producing zero transition nodes.
• The vocabulary matcher was also strengthened during the revision. It now applies single-edit fuzzy tolerance for alphabetic tokens, with ambiguity rejection and numeric exclusion, verified by a set of 26 unit cases.

## Slide 21
Stage 8. Label Placement Measurement
Addresses R1.3, R1.17 - Sections 6.3 and 10.2
21
Reviewer 1 also asked why the label position should serve as the main node, since labels could in principle sit anywhere in a room. We measured the placement across the corpus.
• Across 172 rooms on nine floor sections, the offset between the label position and the geometric centroid of the room's region has a median of 0.24 room-equivalent radii and a worst case of 0.98.
• 92 percent of labels fall inside the room's inscribed circle, so drafting practice does place labels centrally in this corpus.
• The revision reports this measurement as the justification and removes the imprecise term semantic centroid throughout, which also answers R1.17.

## Slide 22
Stage 9. Downstream Task Validation
Addresses R1.1 - Section 10.9
22
To answer the question of what the graph is for, the revision performs two navigation tasks on it directly.
• Step-free routing. Routing with stairs forbidden is expressible because transitions are typed. On the two-floor merge with full correspondence, all 200 sampled cross-floor room pairs remain reachable without stairs, at a mean detour of 1.79 relative to unrestricted routing.
• On the pair where only a stairs correspondence exists, all 102 pairs are reachable normally and none is reachable step-free. The analysis therefore surfaces an accessibility gap that an untyped graph could not express, which illustrates the value of typed transitions concretely.
• Egress analysis. Every room on the evaluation floors has a path to an exit, with a median distance of 901 pixels and a ninetieth percentile of 1,503.

## Slide 23
Stage 10. Baseline Comparison, Setup
Addresses R3.1c - Section 10.7
23
Reviewer 3 asked for a comparison with a competing approach. The revision adds a structure-only baseline, the medial-axis skeleton of free space used as a routing backbone.
• The baseline is deliberately given a favorable setup. It receives our own room and exit detections, so the comparison isolates the routing structure rather than the semantic extraction.
• Both graphs are evaluated on the same room pairs against the same free-space geodesic reference, so the numbers are directly comparable.
• A comparison against a published learned floorplan parser is under investigation, and a structured qualitative comparison is the stated fallback if a fair run proves infeasible.

## Slide 24
Stage 10. Baseline Comparison, Results
Addresses R3.1c - Section 10.7, Table 4
24
Axis | Skeleton baseline | Tesseract graph
Graph size | 3.7 to 12 times more nodes | 878 and 712 nodes
Completeness | 0.78 to 0.83 | 1.000
Route stretch | 1.23 and 1.38 | 1.05 and 1.23
Query time | 37 to 94 times slower | 0.36 to 0.38 ms
Semantics | none | typed rooms, doors, transitions
The skeleton fragments at doorway gaps, which explains its incomplete connectivity, and it cannot express any of the typed downstream tasks. The typed construction is smaller, complete, closer to optimal routes, and faster to query on the same inputs.

## Slide 25
Textual Changes in the Manuscript, Part 1
Sections 1, 3, 9, and 11
25
• The contribution list is repositioned around multi-floor construction and the room-family representation, with door classification presented as a supporting deepening (R3.1a).
• Automation claims in the abstract, introduction, and Section 9 are re-audited to match the implementation, and the remaining metadata assistance, floor indices from filenames, is stated explicitly (R1.9, R2.W1, R3.2).
• The input section now defines an operating envelope, with a label vocabulary table, stated preconditions, explicit exclusions, and a demonstrated failure mode for missing label classes (R3.4, R2.W5).
• Exit doors are defined precisely, the graph is stated to be undirected, and one-way constraints are listed as a limitation with directional attributes as the extension (R2.W4).

## Slide 26
Textual Changes in the Manuscript, Part 2
Sections 2, 3, 5, 6, and 10
26
• The underlying raster representation is stated, all acronyms are introduced at first use, the OCR mechanism is described exactly as implemented, and the term semantic centroid is removed (R1.2, R1.10, R1.11, R1.17).
• A dataset figure shows the evaluation drawings, with full-width reproductions in the appendix (R1.5).
• The misplaced results paragraph is moved into the evaluation (R1.15).
• The related work section is completed, and seven inconsistencies between the earlier text and the implementation were found during the rewrite and corrected, including the segmentation being label-driven rather than color-driven and the correct subnode spacing.
• The full manuscript was swept for grammar, flow, and consistent US spelling, with the checks scripted so they can be repeated.

## Slide 27
The Submission Package
Repository folder paper, ready for Overleaf
27
The paper folder now contains exactly the submission bundle, verified so that every figure, input, and citation resolves inside it.
• initial_submission.tex, the frozen reference of the submitted version.
• main_revision_1.tex, the revised manuscript with reviewer-coded coloring, blue for Reviewer 1, green for Reviewer 2, purple for Reviewer 3, and vermilion for shared points. The coloring works in captions, tables, and titles.
• main_revision_1_clean.tex, the identical manuscript with the coloring disabled by one toggle line.
• response_to_reviewers.tex, in which every response first thanks the reviewer for the specific point, then explains what was done, and then gives the section, subsection, and figure or table location of the change.
• table_of_changes.tex, a fourteen-row summary with locations, plus the bibliography and all nine figure assets.

## Slide 28
Remaining Work Before Submission
Tesseract Journal Extension, Revision 1
28
1. Consolidated dataset runs. The full three-floor site and the restored conference sites run through the existing scripts without code changes, and they provide real precision and recall for the matcher. The manuscript slots are marked and waiting.
2. One check against the conference sources. Whether the door classification algorithm changed decides the final phrasing of one contribution (R3.1b).
3. Two figure regenerations that require the submission-era assets (R1.13, R1.16).
4. The first Overleaf compile, followed by filling the page numbers in the response letter and checking figure placement.
5. Acknowledgments text from the authors.
Everything else is complete, measured, and localized. The revision aims to resolve every reviewer concern within this single round.